## Slide 1: Deriving the RC Circuit Model
KVL
Ohm's Law
KCL
Capacitive Current
R
C
VS

## Slide 2: Deriving the RC Circuit Model
R
C
VS
Voltage across the capacitor as a function of time
KVL
Ohm's Law
KCL
Capacitive Current

## Slide 3: The rc_decay Circuit
D4
A1
+3.3V
10KΩ
10F
A1
GND
We are measuring via an ADC the
voltage drop across the resistor
Pin D4 → DAC mode
Pin A1 → ADC mode

## Slide 4: Big Picture of rc_decay Lab
Waits for a serial (USB) port connection from the laptop
Connects to the KB2040 over the serial (USB) port
Waits for the command "r" to be sent by the laptop over the USB (CDC Data) port
Sends the string "r" to the KB2040 over the CDC Data port
Sets NeoPixel to BLUE to fully discharge capacitor, then to RED as it recharges the circuit while measuring volts & times
Waits to receive the volts and times from the KB2040
Sets NeoPixel to YELLOW as it sends the volts and times to the laptop over the USB port
Plots the voltage vs. time graph for the RC circuit and saves a PNG file of the plot window
code.py running on KB2040
rc_decay.py running on Laptop
NeoPixel is GREEN

## Slide 5: Step 05 – KB2040
(1) KB2040
(1) USB Cable
+3.3V
GND

## Slide 6: Connect the KB2040

## Slide 7: The DAQ device is working…
Discharging
before starting
Measuring circuit voltage over time

## Slide 8: Run rc_decay.py

## Slide 9: Check rc_decay.py