## Slide 1
Student #1
Student #2
Student #3
Control Systems
Engineering
(CSE 201)
Team 08
RLC Resonance
Inductors & Impedance

## Slide 2: Our Challenge: Model an Inductor Circuit
An inductor is a passive two-terminal electrical component that stores energy in a magnetic field when electric current flows through it. An inductor typically consists of an insulated wire wound into a coil
When the current flowing through the coil changes, the time-varying magnetic field induces a voltage which opposes the change in current that created it. As a result, inductors oppose any changes in current passing through them

## Slide 3: An Analog to Simple Harmonic Motion
An inductor can store electrical energy in its magnetic field, so when the circuit needs power, an inductor can draw energy from its stored magnetic field to quickly resupply the circuit

## Slide 4: Modeling an RLC Circuit
Our challenge was to plot the current over time flowing through an RLC circuit that maintains a constant DC voltage
We used the Euler-Cromer method to estimate this 2nd-order homogenous ODE for one second using the given component values
The circuit started with one amp of current, but due to heat loss in the resistor, the energy in the circuit decayed from its initial maximum value
R = 0.1 Ohms
L = 0.01 Henries
C = 0.01 Farads
Initial I = 1 Amp

## Slide 5: Our Solution







Rewrite 2nd-order ODE as two linked 1st-order ODEs

## Slide 6: Our Solution








## Slide 7: Our Results
Lacking additional energy, the circuit's power drains away as it transforms into heat within the resistor.

## Slide 8: Our Results
Every RLC circuit has a specific fixed fundamental frequency in which it oscillates based on its
L and C values

## Slide 9: Driven Physical Oscillators - Resonance
A system driven at its resonant frequency will experience maximum amplitude

## Slide 10: Driven Electrical Oscillators - Resonance
At the resonant frequency, the capacitive reactance in the LC components equals the inductive reactance, and therefore their impedance drops to zero – all that remains is the resistance of the R, L, C components
0

## Slide 11: Modeling a Driven RLC Circuit
Charge (in Coulombs)
Current (in Amps)
S
R
L
C
AC Voltage Source
Ohm's Law
Faraday's Law
Gauss's Law
Kirchhoff's Voltage Law
10.05Ω 99.32Ω
100.8mH
91.2
uF
Euler's Method
Voltage across the resistor

## Slide 12: Our Revised Solution











## Slide 13: Our Revised Solution










## Slide 14: Our Revised Results
At resonance, the LC elements have nearly zero resistance, so the current (and hence voltage) flowing through R1 (and R2) would be at the maximum

## Slide 15: Checking Our Results

Euler's Method is only 1st order accurate and susceptible to stability issues with oscillating signals

## Slide 16: Team 08 – What We Learned
Inductors store electrical energy in a magnetic field
An inductor’s impedance is like a resistor’s resistance because they both oppose current flow in a circuit
Without a voltage source driving an RLC circuit, the initial energy will drain away due to heat loss in the resistor, but the circuit will still oscillate even while the voltage decays to zero
However, if an RLC circuit is continuously driven with a sinusoidal voltage source, there is a specific frequency at which the RLC circuit will resonate, meaning it will achieve the maximum possible voltage